## Slide 1: Testhead OS V2.2.5 Note

## Slide 2: V2.2.4 format of tab & limit file
The attached file are table file and limit file of MT6169 for Testhead OS V2.2.4
The format of Table File was as follows :
Test ID | User Function | Test Name | Hardware Bin Number | Bin Type
110 | Default | digital_opens | 4 | F
The format of Limit file was as follows :
TestID | Test Name | Item Name | Pin Name | Pattern | Low Limit Type* | Low Limit | High Limit Type | High Limit | Unit | User Funciton | Software Bin Number | Software Bin Name
110 | digital_opens | continuityPositive | BSI_CK | (null) | 1 | 0.25 | 2 | 1.2 | V | Default | 1003 | digital_opens
*Limit Type: 1: Greater, 2: Less, 3: Equal than, 4: Equal less

## Slide 3: V 2.2.5 format of tab & limit file
The attached file are table file and limit file of MT6176 for Testhead SGOS V2.2.5
The difference of V2.2.4 & V2.2.5 is the hardware bin number and bin type move to limit file.
The hardware bin name also added to limit file for future use.
The format of table file for V2.2.5 is like as follows:
Test ID | User Function | Test Name
110 | Default | digital_opens
The format of limit file for V2.2.5 is like as follows:
TestID | Test Name | Item Name | Pin Name | Pattern | Low Limit Type* | Low Limit | High Limit Type | High Limit | Unit
110 | digital_opens | continuityPositive | BSI_CK | (null) | 1 | 0.25 | 2 | 1.2 | V
~
~
User Function | Hardware Bin Number | Hardware Bin Name | Software Bin Number | Software Bin Name | Bin Type
Default | 4 | (null) | 1003 | Digital_opens | F

## Slide 4: Testhead SGOS V2.2.5 note
V2.2.5 is only for MT6176 right now.
If MT6169 need run under V2.2.5, it’s just need to modify the format of MT6169 table and limit file as V2.2.5 required. Don’t need re-compile the test program of MT6169.

## Slide 5: Difference of testhead OS & Standard OS
There are two difference:
I. The format of table file (*.tab) & limit file (*.lim).
II. The way to deliver test values from test program to OS main program.

## Slide 6: Difference of testhead OS & Standard OS
Standard OS :
Test Item in tab file must map to the item in limit file.
Ex. Table file Ex. Limit file
Notes: 在Standard SGOS中, Table file所列的test item其test id都皆對應到Limit file中的每一項test id.
所以對Standard SGOS來說, Table file的每一列及代表一個Test Item

## Slide 7: Difference of testhead OS & Standard OS
Testhead OS:
For digital Testing, the format of table & limit file has a “group” item.
The test item in tab file could be a test item group.
The test item in limit file could be set a single pin or group pin.
To see the example file at the page 3 of slides.
To achieve the test item group, it need memory filemapping to deliver test values from test program to SGOS Main program.
Notes: Testhead OS為了能夠對應Digital測試中動輒2,30 pins的需求, 將table file中的每一test item可以視作一個test group.
一個測試item, 可以同時測試多個相同spec的pins並一起回傳結果給主程式
而Limit file中, 可以透過Pin Group概念將多個相同spec的pin 一起設定limit, 或將每一根pins視為獨立來設定limit判定.
為了達成test item group, 主程式與測試程式傳遞test values的方式則比須改為memory file maping的方式來進行傳遞

## Slide 8: The way to transfer test values
In Standard SGOS, the way to transmit test values is go through the struct TestVar
struct TestVariable //V1.15.1,V1.16.0
{
int LimNum;
int ItemNum;
double **meadata;
int *Transif;
double **TransValue;
double **TestValue;
int *number_site;
unsigned int SiteFlag;
int MaxSite_Num;
int *TestID;
int TestSites;
int PinCount;
int SiteCount;
char *CableLoss;
};
OS
Main Core
Test Program (DLL)
TestVar
Notes: 原本Standard OS與測試程式傳遞資料的方式是透過一個TestVar的陣列, 利用指標來做存取
但這方式僅適用一次傳一個test item的資料, 因為TestValue的個數是固定的

## Slide 9: The way to transfer test values
In Testhead SGOS, the way to transmit test values is by shared memory (file mapping).
/* enum Shared Memory Status:
Before the shared memory is filled with data, status is set to "NOT_READY".
After the shared memory is filled, the server sets status to "FILLED".
Then, the server waits until status becomes "TAKEN", meaning that the client has taken the data.
*/
enum eShmStatus{FILLED, NOT_READY, TAKEN};
struct strMeasValue {
char TestName[100];
char Item[100];
char PinName[100];
double TestValue[SITES];
};
struct SG_RETURN_RESULTS {
eShmStatus Status;
strMeasValue MeasValue[150];
int ItemNum;
};
Share memory
(SG_RETURN_RESULTS)
OS
Main Core
Test Program (DLL)
Notes: 在testhead SGOS中, 傳遞test vlues是透過shared memory的方式
此一方式可以一次傳遞多個test items的資料, 因此可以傳遞一個group的test item, 適合digital testing的特性需求, 一次傳多個pin的資料.

## Slide 10: Memory file mapping
To use filemapping & MapViewOfFile
I. Type define:
II. Create object:
static void* lpvMem = NULL; // pointer to shared memory
static HANDLE hMapObject = NULL; // handle to file mapping
const char szMapObject[] = "SG9000MemFileMap"; // name of mapping object
SG_RETURN_RESULTS strResult;
SG_RETURN_RESULTS *ShaMem;
ShmSize = sizeof(strResult);
hMapObject = CreateFileMapping(INVALID_HANDLE_VALUE, NULL, PAGE_READWRITE,
0, ShmSize, szMapObject);
if (hMapObject == NULL) {
MessageBox(NULL, "Could not create file mapping object",
"Warning...", MB_OK);
return;
}
lpvMem = MapViewOfFile(hMapObject, FILE_MAP_ALL_ACCESS, 0, 0, 0);
if (lpvMem == NULL) {
MessageBox(NULL, "Could not map view of file", "Warning...", MB_OK);
return;
}
Notes: 1. 測試程式要能同樣讀取這塊在記憶體中開出來的file mapping, 是由上列中 “szMapObject” 所記錄的名稱 “SG9000MemFilemap”決定, 只要名稱一樣就可以兩邊都讀到同一塊記憶體

## Slide 11: Memory file mapping
III. Usage:
After link SheMem to lpvMem, it could read the member of SheMem by use “SheMem->”
The introduction of file mapping: Windows API一日一練(59)CreateFileMapping和MapViewOfFile函數
SG_RETURN_RESULTS *SheMem;
SheMem = (SG_RETURN_RESULTS*)lpvMem;
Notes: SG_RETURN_RESULTS的member內容可以看ClassSet.h檔
關於filemapping更詳細的介紹可以看網址 http://s.epb.idv.tw/han-shi-ku/windows/win-api-han-shi-shi-yong/mei-ri-yi-lian/windowsapiyiriyilian59createfilemappinghemapviewoffilehanshu

## Slide 12: Large than 2G Limit in Windows
Windows作業系統 (Win XP, 7 , vista, 10)中, 微軟有限制每一執行程式 (App)最多只能使用記憶體到2 GB。而在Testhead SGOS下, 由於測試程式使用的記憶體很大 (大多是Pattern File) , 於是SGOS在整體使用記憶體會超過2GBs。
因此必須在Compile時對Compiler設定讓其能夠超過2GBs。
“-GF:LARGEADDRESSAWARE” 此為讓程式使用超過2GBs的Compile指令設定
1. 修改SG9000.bpr檔案 (可使用NotePad++開啟)
2. 找到”LFLAGS”此一header, 並將以上指令加入如下所示: