## Slide 1: How to add new sitemap in Interface module for UF200 Prober

## Slide 2: Site map
To set interface for multisite testing on prober (UF200), it has to add a site-map identification in “InterfaceGPIB” module at the function: check_orientation().
In SGOS, the co-ordinate of multi-testing is calculate by the location difference from site 1 on site-map.
Ex: See the pic of site-map below, if the coordination is that right and down are positive. Then the coordination of multi-site is likely listed as below.
(0,0)
(0,2)
(-2,0)
(-4,0)
(-6,0)
(-2,2)
(-4,2)
(-6,2)
+
+
X
Y

## Slide 3: Adding Site Map
First, we need to get the “code” for the map which sent from the UF200 (prober).
In the directory: “C:\SG9000II\SYSTEM\”, there is a log file named “InterfaceLog.txt”. It record almost every signal information which communicating between tester and prober.
To find the code of sitemap, you could open that log file then search the word “Error” to find out as below.
The Code is “XG” for the example.

## Slide 4: Adding to Interface module
After getting the site-map code, you would add the co-ordination into InterfaceGPIB module which the function: “check_orientation()”.
As the example listed in page 1, it would add the code like as below: (x_sitev[0], y_sitev[0]) = (0,0)
} else if (!strcmp(orientation_char, "XG")) {
x_sitev[1] = -2;
y_sitev[1] = 0;
x_sitev[2] = -4;
y_sitev[2] = 0;
x_sitev[3] = -6;
y_sitev[3] = 0;
x_sitev[4] = -6;
y_sitev[4] = 2;
x_sitev[5] = -4;
y_sitev[5] = 2;
x_sitev[6] = -2;
y_sitev[6] = 2;
x_sitev[7] = 0;
y_sitev[7] = 2;
MyModuleVar->Config.Site_Flag = EIGHT_TEST;