## Slide 1: SGOS Deploy to Test Floor SOP in CS
Rule:
1. Pick up a tester to update newer version SGOS then monitor 2-3 days.
2. If no related issues in monitored 3 days, upload new version SGOS to auto-update server to auto-update to every tester.

## Slide 2: Export SGOS files for updating using TortoiseHg
選取要匯出的版本
匯出

## Slide 3: Export SGOS files for updating using TortoiseHg
設定匯出的目錄位置

## Slide 4: Zip the files
Then select all files and zip as zip file.

## Slide 5: Steps of deploying SGOS to Auto-Update Server
Step 1. Upload the latest SGOS zipped file to server by FTP client.
Step 2. Rename the older SGOS zipped file on server. (NewOS.zip -> OldOS.zip).
Step 3. Rename the uploaded SGOS zipped file to NewOS.zip.
Step 4. Set the correct version number in StandardOSAutoUpdate.ini

## Slide 6: Auto-update server
FTP Server:
IP : 192.168.32.16
Account : RDprogeng
Password : Rdeng010
FTP Contol Path:
rdtopeprog_folder/SG9000 OS AutoUpdate/

## Slide 7: Auto-Update Server Note
在SG9000 OS AutoUpdate資料夾下必須要有OS Main和以Tester為名稱的資料夾
有AutoUpdate的Tester必須在FTP建立出以Tester為檔名的資料夾，用來存各Tester的更新資訊
存放管理AutoUpdate的相關檔案

## Slide 8: Auto-Update Server Note - OS Main Folder
NewOS.zip
  新版OS的壓縮檔
OldOS.zip
  舊版(前一版)OS的壓縮檔
OSUpdateList.txt
  OS的更新訊息(會顯示在AutoUpdate視窗上)
StandardOSAutoUpdate.ini
  控制整個AutoUpdate系統的設定
在OS Main資料夾下，必須包含上列4種檔案

## Slide 9: Auto-Update Server Note - StandardOSAutoUpdate.ini Setting
[VerControl]
OSVer : 目前Tester OS的版本
OSVerControl : 要更新的OS版本
RecoveryOSVerControl : 前一版的OS版本
[Automation]
UpdateFile : 新版OS在Server上的位置
RecoveryFile : 前一版OS在Server的位置
LocalFile : 從Server下載到Tester的位置

## Slide 10
[UpdateControl]
OpenServerUpdate : 允許Server上的新版OS可更新至Tester (ON/OFF)
OpenTesterUpdate : 開啟Tester端AutoUpdate功能 (ON/OFF)
OpenRecoveryUpdate : 開啟Server上Recovery Update功能 (ON/OFF)
[UpdateTime]
WeekDateType : 固定於某日或某範圍日內更新 (Above/Between)
HourType : 固定於某小時或某小時範圍內更新 (目前只有Between)
WeekDateStart : 要更新的開始日
WeekDateEnd : 要更新的截止日 (若WeekDateType為Above, 不判斷這項)
HourStart : 要更新的開始小時
HourEnd : 要更新的截止小時
***WeekDate : 代表星期幾，1:星期天, 2:星期一, 3:星期二,…… 7:星期六
(use DayOfWeek function)
WeekDateStart=2 (星期一)
WeekDateEnd=6 (星期五)
代表從星期一到星期五都會執行AutoUpdate
Auto-Update Server Note - StandardOSAutoUpdate.ini Setting

## Slide 11: AutoUpdate Flow Chart
FTP :
OSVer = new OS Version
OpenSerUpdate = ON
OpenTesterUpdate = OFF
OpenRecoveryUpdate = OFF
Tester :
AutoUpdate = ON
FTP :
OSVer change to last Version
OpenSerUpdate change to OFF
OpenTesterUpdate change to OFF
OpenRecoveryUpdate change to ON
Tester :
AutoUpdate change to OFF
FTP :
OSVer change to new Version (administrator setting)
OpenSerUpdate change to ON (administrator setting)
OpenTesterUpdate change to ON (administrator setting)
OpenRecoveryUpdate change to OFF (administrator setting)
Normal Condition
After Recovery OS
After debugging and resetting