## Slide 1: SGOS Checked Procedure for new build/modified SG9000 Tester

## Slide 2: SGOS Check Procedure
1. Make sure AutoUpdate installed in tester.
2. Create shortcut of AutoUpdate on desktop
3. Check OSUpdate.ini setting
4. Check SG9000II.ini setting
5. Check interface type setting
6. Check EndLot.txt
7. Check SGSeting.ini

## Slide 3: SGOS Check Procedure
1. Make sure AutoUpdate installed in tester.
2. Check OSUpdate.ini setting

## Slide 4: SGOS Check Procedure
OSUpdate.ini
*Condition = CP or FT
*AutoUpdate= ON or OFF

## Slide 5: SGOS Check Procedure
1. Create shortcut of AutoUpdate.exe to desktop.
2. Rename the name of shortcut as “SG9000II.exe”.

## Slide 6: SGOS Check Procedure
1.Check OSVersion.
2.Check SG9000II.ini content and setting

## Slide 7: SGOS Check Procedure
SG9000II.ini
[Tester]
Name=TSG80 #Tester No.
OSVer=V1.17 #OSVer
OSVerControl=V1.17.0.0018 #VerControl setting for auto-update
#if version number less than version on SGOS server, it will activate autoupdate procedure.
Interface=DAQ7432 #It decide what kind of interface to connect Handler
(DAQ7432. DAQ7230, DAQ6509, GPIBEPSON, GPIBUF200)
SetupPW=OFF #Turn on/off the password form of Setup Page
[Automation]
BarCode=P:\Xml\TSG80\Tester_barcode.xml #Indicate the location of Barcode file(Xml) for Autoload

## Slide 8: SGOS Check Procedure
Check Interface Type in SG9000II.ini.
SG9000 could use the interface type as follows:
1. DAQ7432, DAQ7230 – ADLink PCI Card for TTL, Connect Bow feeder Handler for Final Testing
2. DAQ6509 – NI 6509 Card for TTL, connect Bow feeder Handler for Final Testing
3. GPIBEPSON – GPIB Card for Pick-n-Place Handler, Connect EPSON N-Series Handler
4. GPIBUF200 – GPIB Card for Prober, Connect UF200 Series Prober.

## Slide 9: SGOS Check Procedure
Check EndLot.txt in /SYSTEM/Customer/ directory.
1. Put the filename of execute program when End-Lot into EndLot.txt
2. The content of EndLot.txt is customer related.

## Slide 10: SGOS Check Procedure
Check SGSetting.ini in /Utility directory.
1. It’s related to the “Customer’ set in SPJT file and the AutoLotID module to know use which customer’s file rule
2. The key “Customer” mean customer name store as same as in SPJT file and split by comma.
3. The key “CustomerNo” mean the number indicate which customer that same as in barcode file.